## Slide 1: Lecture 2 Biotechnology Product Development Pathway
BIO 3112 – Biotechnology Product and Formulation
Dr. James H. Kimotho, PhD

## Slide 2
Stage-Gate Model applied
Biological resource and molecular biology = Pre-upstream (R&D)
Fermentation = Upstream
Purification = Downstream
Large-scale production = Scale-up of both

## Slide 3: Stages 1–2: Discovery & Molecular Engineering
Stage | Key Activities | Supportive Activities
1. Biological Resource | Organism selection Examples E. coli → fast growth, simple proteins Chinese Hamster Ovary (CHO)→ monoclonal antibodies (85% of biopharmaceuticals) Yeast → vaccines and enzymes Plants → secondary metabolites / recombinant proteins Does it perform necessary post-translational modifications? Glycosylation (mammalian systems) Disulfide bond formation Protein folding capability Gene dentification (and validation of the genetic sequence responsible for the desired product) | QMS Risk mgmt. IP Regulatory review
2. Molecular Biology | Cloning Vector design Host selection Expression option . | GLP Design control Data integrity

## Slide 4: Stages 3–4: Bioproduction & Purification
Stage | Key Activities | Supportive Activities
3. Upstream Processing | >Fermentation Used for: Enzymes, Recombinant proteins Vaccines, Antibiotics, Common organisms: E. Coli, Yeast (Saccharomyces cerevisiae), Fungi Advantages: Fast growth, High productivity, Lower cost, Robust systems Limitations: Limited post-translational modifications Endotoxin concerns (Gram-negative bacteria) > Mammalian Cell Culture Used for: Monoclonal antibodies, Complex glycoproteins, Advanced biologics Common cell lines: CHO cells, HEK293, Vero cells Advantages: Proper protein folding, Human-like glycosylation Limitations: Slower growth, More sensitive to shear stress, Higher cost > Media option > pH/temp/O₂ > Scale up | QbD (Quality-by- Design) PAT = Process Analytical Technology [Real-time measurement, monitoring, and control of critical process parameters (CPPs) and critical quality attributes (CQAs)]. Contamination control

## Slide 5
4. Downstream Processing | Filtration Chromatography Impurity removal Buffer exchange | Process validation Analytical validation QMS

## Slide 6: Stages 5–6: Formulation & Clinical Development
Stage | Key Activities | Supportive Activities
5. Formulation | Adjuvants (for vaccines) Buffers Excipients Stability testing Packaging | Stability protocols Risk analysis Regulatory planning
6. Clinical Trial | Phase I–III Safety monitoring Data mgmt | GCP Ethics approval Regulatory submission

## Slide 7: Stages 7–8: Production & Market Use
Stage | Main Purpose | Key Activities | Supportive Activities
7. Production | Commercial manufacturing | GMP manufacturing Batch testing Fill-finish End-to-end | QA/QC Audits Documentation
8. End User / Market | Safe delivery & lifecycle mgmt | Distribution Pharmacovigilance Post-market surveillance | QMS Cold-chain control Recall systems