## Slide 1
Lecture 3
PAUSTI MSc Mol Biology Class
Recovery and Purification of Bio-products
1

## Slide 2
Key areas in development, production, and commercialization of biotherapeutics
Drug Product

## Slide 3: Estimated cost contribution of Research-to-Commercialization (R2C) of bioproducts
Research and Development (R&D): 20 - 40%
Raw Materials: 20 - 40%.
Production Facilities: 10 - 30%
Purification Process: 10 - 30%
Quality Control: 5 - 15%
Regulatory Compliance: 5 - 15%
Marketing, Storage and Distribution: 5 - 10%

## Slide 4: Industrial Recovery and Purification of Bio-products
(From WCB)

## Slide 5: Cell disruption

## Slide 6
The breaking of cell envelop (membranes & cell walls). This releases the intracellular content into the medium
Mechanical
  Ultrasonication
  Milling e.g. with beads, impeller blades
  Homogenization e.g. high pressure homogenizer where cell disrupts as they are extruded
through an orifice.
Non-mechanical
  Chemical – use of chemicals to solubilize the components of the cell walls to release the product.
    Examples of chemicals: surfactants such as sodium sulphonate, alkali such as sodium hydroxide, toluene (that penetrate the lipid layer swelling the cell causing disruption.
  Enzymes
    Lysozyme
  Osmotic shock
    Use of pure water
The process should NOT damage the product

## Slide 7: Supernatant, Recovery and Purification

## Slide 8: Separation of soluble products…1
Liquid-Liquid Extraction
  In bio-production, the heavy phase is fermentation broth
The light phase is the organic solvent e.g. Isoamyl acetate
These organic solvents are immiscible with the culture broth and are non-toxic
Product to be isolated must have high distribution coefficient in the light solvent
Kd = YL/XH: YL concentration in the light solvent/Concentration in the
heavy solvent
Light, YL
Heavy, XH

## Slide 9: Separation of soluble products…2
Precipitation
  This is done using inorganic salts such as:
    Ammonium Sulphate
    Sodium Sulphate
  They act by increasing the ionic strength, the salt interacting more with water hence precipitating proteins and other large molecules
  This precipitation is affected by:
    pH
    Temperature
  Proteins are usually precipitated at their Isoelectic points

## Slide 10: Separation of soluble products…3
Adsorption
  Soluble products from fermentation broth onto solids
  It is determined by difference in affinity of a product in solid and liquid phase
  It is influenced by
    Ionic strength
    pH
    Temperature
    Nature of solutes
  It can either be based on physical adsorption or ionic adsorption
  Example: DNA extraction using silica gel/beads

## Slide 11: Separation of soluble products…4
4. Centrifugation
Centrifugation is a process by which solid particles are sedimented and separated from liquids using centrifugal forces as the driving force.
There two major types of centrifugation
  Differential centrifugation
    It used the principle of separation using different speeds AND different times. Once the 1st
separation the next is started with the same sample.
    It used to separate cell organelles
  Density gradient centrifugation
    Separation depends density, shape and size
      Rate zonal centrifugation (density, shape and size)
      Isopycnic centrifugation (density)

## Slide 12: Separation of soluble products…5
Chromatography
  This technique involves separation of mixtures due to the differences in the distribution coefficient of sample components between two phases: stationary and mobile phases.
  The two main types of chromatography are:
    Ion Exchange Chromatography (based on charges)
    Affinity Chromatography (based on affinity of binding sites on the protein

## Slide 13: Separation of soluble products…6
Filtration
  Separation of particles from the liquid by applying pressure to the solution to force a solution through a filter/membranes
  The two main types of filtration are:
    Dead end filtration
      All the flow are directed through the membrane with materials building up on the surface of the filter causing clogging and failure to flow
    Tangential filtration (Cross Flow Filtration)
      Fluid is recirculated in tangential flow parallel to the filter membrane
      Build up of viral particles on the membrane is reduced

## Slide 14: Separation of soluble products…7
Membrane filtration can be
  Microfiltration
    Usually 0.1-10uM
    Normally used in sterilization of heat sensitive products such as bacterial & yeast
  Ultrafiltration
    Mainly used in separation of macromolecules of MW 2000 – 500,000 D
  Dialysis
    Removal of low molecular weight solutes, inorganic ions and inorganic acids MW 10- 500

## Slide 15: Separation of soluble products…8
7. Electrophoresis
This is used to separate charged solutes based on their specific migration rates in a electric field
Migration is determined by:
  Electric charge of the solute
  Electric field strength
  Particle size
  Viscosity of the liquid

## Slide 16: Separation of soluble products…7
Membrane filtration can be
  Microfiltration
    Usually 0.1-10uM
    Normally used in sterilization of heat sensitive products such as bacterial & yeast
  Ultrafiltration
    Mainly used in separation of macromolecules of MW 2000 – 500,000 D
  Dialysis
    Removal of low molecular weight solutes, inorganic ions and inorganic acids MW 10- 500

## Slide 17: 8. others
Crystallization
  This is usually the last step of producing highly purified product such as antibiotics
  The solution is supersaturated and stored at low temperature after which crystals are separated by use of filters
Drying
  Of heat sensitive is by:
    Freeze drying
    Vacuum drying
    Spray drying [Spray drying is a method of producing a dry powder from a liquid or slurry by rapidly drying with a hot gas e.g. milk powder, coffee, and antibiotics]